## Slide 1
Making KV Movement Agent-Aware
Coding agents naturally pause during tool calls, then resume with tight latency expectations. Current memory movement paths are largely context-agnostic: they can move KV pages, but they do not know which agent needs them, when they are needed, or whether missing the deadline will stall replay. This project aims to quantify that gap and prototype hint-guided KV movement as a path toward smarter DMA engines, KV-aware memory scheduling, and hardware/runtime co-design.
model turn
→
tool wait
→
replay request
→
KV ready?
Agent-aware KV movement
01
Notes: Opening slide. Position this as a hardware/runtime co-design question, not just an SGLang software optimization.
Goal: Coding agents naturally pause during tool calls, then resume with tight latency expectations. Current memory movement paths are largely context-agnostic: they can move KV pages, but they do not know which agent needs them, when they are needed, or whether missing the deadline will stall replay. This project aims to quantify that gap and prototype hint-guided KV movement as a path toward smarter DMA engines, KV-aware memory scheduling, and hardware/runtime co-design.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 2
The testbed uses both controlled and real agent traffic
Synthetic request generators give clean knobs; SWE-bench/DeepAgents traces give realistic coding-agent behavior.
Controlled synthetic path
Synthetic request generator creates known prompt sizes, tool-wait windows, filler pressure, and replay deadlines.
Real coding-agent path
SWE-bench / AgentBench tasks feed DeepAgents, which emits model turns and tool-call gaps into SGLang.
Source: latest_master_report.html, Experiment Setup And Manager Summary
Agent-aware KV movement
02
Notes: This slide explains the two traffic feeds. Synthetic runs let us control pressure and timing; real DeepAgents/SWE-bench traces preserve realistic coding-agent prompts and tool gaps.
The setup flow image comes from latest_master_report.html.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 3
The prototype runs real prompts through SGLang
Concrete setup behind the charts: traffic source, serving stack, one GPU, model, and host-side KV cache.
Synthetic
request generator
→
SWE-bench /
DeepAgents traces
→
SGLang
OpenAI server
→
Qwen Coder
7B Instruct
→
GPU KV cache
+ HiCache
GPU
NVIDIA A10G class
GPU memory
24 GB GDDR6
HiCache host KV shelf
16 GB configured
Context length
32,768 tokens
Max total tokens
12,288
Memory fraction static
0.72
Tensor parallel
TP = 1
HiCache policy
direct + write-through
Source: latest_master_report.html setup section and run configuration
Agent-aware KV movement
03
Notes: This slide summarizes the concrete prototype setup used for the current manager report.
Hardware/runtime values are from the latest master report setup section and the project run configuration: Qwen2.5-Coder-7B, A10G-class single GPU, 24 GB GDDR6 GPU memory, 16 GB HiCache host KV shelf, context length 32768, max total tokens 12288, mem fraction static 0.72, tensor parallel size 1.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 4
Today’s DMA engines move bytes, not intent
The hardware path is fast, but it usually lacks agent/session semantics.
Context-agnostic movement
sees memory ranges
does not know the agent session
does not know replay deadline
does not protect useful prefetched KV
→
Hint-aware movement
tags KV by session and priority
schedules against replay deadlines
moves hot KV before replay
reports late, useful, and wasted movement
Agent-aware KV movement
04
Notes: This slide frames the hardware opportunity: hints must become enforceable by the memory movement path.
Hardware examples include SDMA, CPU-side DMA, NIC DMA, SSD DMA, and copy/migration engines.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 5
The replay path exposes the bottleneck
Several tool-gap sessions show where replay spends time before the first useful token.
Source: latest_master_report.html controlled run
Agent-aware KV movement
05
Notes: Use this as the narrative chart. It shows the initial model turn, tool wait, replay path, replay-side H2D, recompute, prefill, and decode.
The image is a cropped view of the Readable Phase Timeline in latest_master_report.html.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 6
Software prefetch often missed the agent replay deadline
Across live prefetch attempts, nearly every hint completed after the agent had already resumed.
112 of 114
prefetch attempts
were late
98.25%
missed replay due deadline
This shows that semantic knowledge alone is not enough if the movement path cannot act on hints predictably.
Source: backups/latest_master_report-1.html, Global Prefetch Margin
Agent-aware KV movement
06
Notes: This slide is the global prefetch-attempt evidence. The backup report shows 114 matched prefetch attempts, 112 late, and 98.25% late.
Use it to show that software prefetch through the normal serving path often misses tight replay windows.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 7
Replay-side KV loads missed the deadline in this run
The aggregate view shows whether KV H2D finished before or after replay was due.
8 / 8
H2D loads finished late
All visible replay-side KV loads finished below the 0 ms deadline line.
Source: latest_master_report.html, Global Replay H2D Readiness
Agent-aware KV movement
07
Notes: This is the aggregate evidence slide. The current controlled no-prefetch run reports 8 no-prefetch replay H2D gaps and 8 late H2D finishes.
Measured claim source: Global Replay H2D Readiness table and dot plot in latest_master_report.html.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 8
The delay is not just copy time
The request enters normal software/runtime scheduling before visible KV H2D begins.
The stage markers separate submission, SGLang receive, scheduler queue/admit, and visible KV H2D movement.
Source: latest_master_report.html, Replay Queue Timeline vs H2D Start
Agent-aware KV movement
08
Notes: This chart separates replay due, client submit, SGLang receive, scheduler queue/admit, H2D start, and H2D finish.
The key manager takeaway: a hint-aware design should influence scheduling and priority, not merely request more copies.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html

## Slide 9
Hardware support can make hints enforceable
The opportunity is to treat KV as deadline-sensitive memory, not generic bytes.
Runtime hint
session, priority, deadline
→
KV-aware queue
order urgent KV first
→
DMA / copy engine
throttle and prioritize
→
Residency control
protect useful KV
→
Telemetry
late / useful / wasted
Resulting research question
How much replay latency and wasted movement can be avoided when KV movement has session context, priority, deadline, protection, and telemetry?
Agent-aware KV movement
09
Notes: Closing slide. This translates observed software/runtime behavior into concrete hardware support candidates.
Hardware ideas come from the project proposal: KV metadata, deadline-aware queues, priority-aware migration, residency protection, and telemetry.
[Sources]
Local report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/sglang_direct_kv/artifacts/results/latest_master_report.html
Backup report: /Users/oluwolejaiyeoba/Documents/GitHub/agentic_hardware/backups/latest_master_report-1.html